## Slide 1
Peripheral Datasheet

## Slide 2
I | J | K | N | S

## Slide 3: MM Addresses During Loading/Unloading
Name | Base | End
i (ker_row/inp_row/out_row) | 00 | 08
j (ker_col) (inp_col_count/ out_col_count) | 09 | 0F
k (inp_col/out_col) (ker_col_count) (out_MS) | 10 | 18
Number (current_num) (out_LS) | 19 | 1F
Status | 20 | 28

## Slide 4: MM Addresses During Mult
Name | Base | End
i (size_ker_row) | 00 | 08
j (size_inp_col) | 09 | 0F
k (size_ker_col/size_inp_row) | 10 | 18
Number (X) | 19 | 1F
Status | 20 | 28

## Slide 5: Status Register During Loading of Kernel Matrix 0x11
X | X | X | X | X | X | X | X | X | ldout | ldinp | ldker | mfin | mstrt | ldfin | ldstrt
X | X | X | X | X | X | X | X | X | 0 | 0 | 1 | 0 | 0 | 0 | 1

## Slide 6: Status Register During Loading of Input Matrix 0x21
X | X | X | X | X | X | X | X | X | ldout | ldinp | ldker | mfin | mstrt | ldfin | ldstrt
X | X | X | X | X | X | X | X | X | 0 | 1 | 0 | 0 | 0 | 0 | 1

## Slide 7: Status Register During Mult 0x06
X | X | X | X | X | X | X | X | X | ldout | ldinp | ldker | mfin | mstrt | ldfin | ldstrt
X | X | X | X | X | X | X | X | X | 0 | 0 | 0 | 0 | 1 | 1 | 0

## Slide 8: Status Register After Mult 0x08
X | X | X | X | X | X | X | X | X | ldout | ldinp | ldker | mfin | mstrt | ldfin | ldstrt
X | X | X | X | X | X | X | X | X | 0 | 0 | 0 | 1 | 0 | 0 | 0

## Slide 9: Status Register During Output Unload 0x48
X | X | X | X | X | X | X | X | X | ldout | ldinp | ldker | mfin | mstrt | ldfin | ldstrt
X | X | X | X | X | X | X | X | X | 1 | 0 | 0 | 1 | 0 | 0 | 0

## Slide 10: Status Register After Completion/Reset Component 0x0A
X | X | X | X | X | X | X | X | X | ldout | ldinp | ldker | mfin | mstrt | ldfin | ldstrt
X | X | X | X | X | X | X | X | X | 0 | 0 | 0 | 1 | 0 | 1 | 0