## Slide 1
Deliverables

## Slide 2: 1) Trained Model
Using TensorFlow libraries, we trained a model that is based on the MobileNet V1 architecture, which can classify Tomato, Apple and Corn plants and their diseases.

## Slide 3: 2) Custom CNN Implementation
A low level CNN implementation that supports MobileNet V1 developed using Python.
Supports vectorization and a parallel framework.
A delta approach of unifying the standard Conv2D & DW Conv2D into one vectorized and parallel algorithm.

## Slide 4: 3) Custom Single Purpose Processor
A low level Matrix Multiplication component developed in VHDL as outlined in MMUL_BLOCK.
Functional simulation testbench.

## Slide 5: 4) System Functional Simulation
A software functional simulation that implements Model & Component interfacing was designed as outlined in: 6- System Block.
Realistic emulation achieved via the use of threading libraries developed in Python.

## Slide 6: 5) Custom Peripheral
Custom peripheral was designed as outlined in: 7- Peripheral Datasheet.
Design of custom protocol for memory loading/unloading and for our custom SPP top level control.

## Slide 7: 6) Avalon Bus MM Interface
Avalon Bus MM Interface allowed for:
HPS (Master) to Peripheral (Slave) interfacing.
FPGA (Master) to Peripheral (Slave) interfacing.

## Slide 8: 7) System Implementation
Two system implementation iterations were developed on DE10 board.
Where the MMul component’s memory is made of:
Registers.
BRAMs.

## Slide 9: 8) Metrics
Runtime
System summary
Component memory utilization
Max clock frequency

## Slide 10: 9) Diagrams
System block diagram
Matrix Multiplication block diagram
Avalon & Peripheral interconnects
Peripheral block diagram
Evaluation of Model

## Slide 11: 10) Documentation
Functional Simulation
  Installation
  Evaluation
  Simulation Notes
Model
  Memory requirements
Peripheral
  HPS-FPGA (General Flow)